## Slide 1: Objectives
Introduction to Remote Sensing
Terminology of aerial photographs
Displaying multispectral images

## Slide 2: Terminology of aerial Photographs
Vantage point
Flight height
Scale
View angle
Ground coverage
Introduction to Remote Sensing

## Slide 3
Camera systems
  use a lens (B)
  to acquire a snapshot of an area (A), and
  to form an image at the focal plane C.
Camera systems are passive optical sensors that

## Slide 4
Vantage point = Camera orientation
The orientation of the camera relative to the ground during acquisition.
  vertical
  oblique
Vantage point

## Slide 5
Vertical aerial photography
A vertical photograph is obtained when the camera’s optical axis is within 3° of being vertical to the Earth surface.
optical axis
Used to create planimetric, topographic, and orthophotomaps, and DEMs using fundamental photogrammetric principles.
less distortion

## Slide 7
Oblique aerial photography
more distortion
An oblique aerial photograph is obtained if the camera’s optical axis deviates more than 3° from vertical.
optical axis
Useful for covering very large areas in a single image and for depicting terrain relief and scale.

## Slide 10
Altitude of the camera above ground level (AGL), for a given focal length
  the higher the altitude, the larger the area
  the lower the altitude, the smaller the area
Flight Height (Altitude)
H1
f
H2

## Slide 11
Photo Scale (S) = Distance on Photograph
Distance on the ground
For an aerial photograph, scale is:
S = camera focal length (f)
flying height above terrain(H)
Scale
Scale can be denoted as
Verbal scale: 1 cm equals 1 km
Representative fraction: 1/100,000, or Ratio scale:1:100,000
Graphic (bar) scale:
4
0
0
4
0
8
0
M
i
l
e
s

## Slide 12
The field of view of a camera
View Angle
Giving the same flight height, viewing angle is determined by the focal length.
The smaller the focal length, the larger the view angle
f1 > f2 > f3
a1 < a2 < a3

## Slide 13
The actual area on the ground that one air photograph covers. Determined by the altitude and the camera’s viewing angle.
Ground Coverage

## Slide 14: The advantage and disadvantage of aerial photography (film)
Introduction to Remote Sensing
Advantages:
High resolution (ground)
Flexibility
High geometric reliability
Relatively inexpensive
Disadvantages:
Day light exposure (10:00 am- 2:00 pm) required
Poorer contrast at shorter wavelengths
Film non-reusable
Inconvenient
Inefficient for digital analysis

## Slide 15
Panchromatic imaging
With panchromatic imaging, the sensor is a single channel detector sensitive to radiation in a broad wavelength range.
Where the wavelength range coincides with the visible range, the resulting image resembles a "black-and-white" photograph.

## Slide 16
Multispectral Imaging
With multispectral, or multiband data, there are several layers, or values for each pixel, each representing a different “channel/band” or reflectance in a wavelength spectrum.
Each “band” or “channel” is sensitive to radiation within a different band of wavelength, through use of different filters.

## Slide 17
Displaying multispectral bands separately
These bands can be looked at separately.
One band from a multispectral image would be displayed as a grayscale image, with each pixel represented by a grayscale value.
blue
green
red

## Slide 18
Displaying multispectral bands (2)
These bands can be combined to make “composite” images.
Composite images are usually displayed by assigning three of the bands to the red, green and blue channels and displaying them additively.

## Slide 19
additive primaries: red, green, and blue
subtractive primaries: cyan, magenta, and yellow
Color types
Additive and subtractive colors
Blue+Green+Red = White Yellow+Magenta+Cyan = Black
Displaying image is based on additive mixing of primary colors, whereas color photography is based on subtractive mixing of complementary colors.
Light mixing follows this
Dye mixing follows this

## Slide 20
Bands are assigned to color channels in such a way that colors in the image roughly correspond with the colors in the real world. Often assigned red to red, green to green and blue to blue can result in this.
True color composite
Band Composite Output =
BLUE
GREEN
RED
NEAR IR
SHORT
WAVE IR
MID-
WAVE IR
LONGWAVE IR
1
Landsat TM Band
2
3
4
5
7
6
Band Combination =
3
2
1 (LANDSAT)
Color Guns =

## Slide 21
Shows colors that don’t really exist in that location. An example is color infrared composite, where green band is assigned to blue display channel, red is assigned to green and Near IR is assigned to red.
False color composite
BLUE
GREEN
RED
NEAR IR
SHORT
WAVE IR
MID-
WAVE IR
LONGWAVE IR
1
Landsat TM Band
2
3
4
5
7
6
Band Combination =
4
3
2 (LANDSAT)

## Slide 22
False color composite
BLUE
GREEN
RED
NEAR IR
SHORT
WAVE IR
MID-
WAVE IR
LONGWAVE IR
1
Landsat TM Band
2
3
4
5
7
6
Band Combination =
4
3
2 (LANDSAT)
Color Guns =
Band Composite Output =