## Slide 1
Understanding airspace and aeronautical maps
Weather/
Reading Sectional Charts

## Slide 2
UAS operators are REQUIRED to obtain prior authorization before operating in any* controlled airspace
*except for some class E airspaces

## Slide 4
Relevant Acronyms
AGL: Above Ground Level
MSL: Mean Sea Level, elevation above sea level
Source: www.flyeye.io/drone-acronym-agl/

## Slide 5
Class A Airspace
FL 180 ft MSL – FL 600 ft MSL

## Slide 8
CTAF
Common traffic advisory frequency
ATIS
Automatic terminal information service
AWOS
Automated weather observing information
Elevation
ASOS
Automated surface observing information

## Slide 10
Class B Airspace
SFC– 10,000 MSL
B = BIG
B = BUSY

## Slide 11
Solid blue lines on a sectional chart

## Slide 12
Logan International Airport, Boston, MA

## Slide 13
Logan International Airport, Boston, MA
All altitudes are in MSL unless indicated in parentheses
SFC = surface
Add 00 to numbers

## Slide 14
Would you need prior authorization to fly around this tower?
San Francisco International Airport

## Slide 15
Class C Airspace
SFC– 4,000 AGL
5 NM
10 NM
4000 AGL
1300 AGL

## Slide 17
Solid magenta lines on a sectional chart

## Slide 18
Syracuse Hancock Intl
All altitudes are in MSL unless indicated in parentheses
SFC = surface
Add 00 to numbers

## Slide 19
Class D Airspace
SFC– 2,500 AGL

## Slide 20
Dubuque Regional Airport, Iowa
36
Airspace ceiling is 3600 ft MSL
Blue-dashed line

## Slide 21
Class E Airspace
1SFC– (designated)
2700+ ft AGL
31200 ft AGL not designated

## Slide 22
Class E surrounding Class C airspace

## Slide 23
Class G Airspace
All uncontrolled airspace up to 1200 AGL
FAA provides no services

## Slide 24
CLASS C
318’ MSL
400’
718’ MSL

## Slide 25
According to 14 CFR part 107 the remote pilot in command of a small unmanned aircraft planning to operate within Class C airspace…
#3
Is required to receive ATC authorization.
Is required to file a flight plan with FAA.
Must use a visual observer.

## Slide 26
700 ft AGL
398’ MSL
400’
798’ MSL
Class E non-designated

## Slide 27
WEATHER and FLIGHT

## Slide 28
The RPIC is REQUIRED to check the weather before flight
SkyVector Flight Planning
Aviation Weather Center

## Slide 29
Convective SIGMETs: significant meteorological information. Severe thunderstorm

## Slide 30
METAR: meteorological aerodrome report

## Slide 31
Station location
15th day of month
12:35 zulu
Automated report

## Slide 32
Winds coming from 10° TRUE
Speeds of 11 knots
Visibility is 10 statute miles
Overcast with cloud ceiling at 1100 ft AGL

## Slide 33
Temperature °C
Dewpoint (M = minus)
Calculate cloud ceiling
* 1000 ft
* 1000 ft

## Slide 34
300’
* 1000
* 1000 = 400 ft AGL
You cannot fly under these conditions because regulations state you must be 500 ft below the cloud base.
50’
50’